## Slide 1: ExaO: Software Defined Data Distribution for Exascale Sciences

## Slide 2: Background (TODO: change figure, add datasize)
Large raw datasets are collected from LHC at the Tier-0 site.
RECO and AOD datasets are distributed to Tier-1 sites for secure storage.
RECO, AOD and simulation datasets are transferred among Tier-1, Tier-2 and Tier-3 sites for analysis.

## Slide 3: Data transfer services in CMS
Dataset level source selection
  Decide sources for all files at once
  Destination sites are treated only as consumers
Built on top of traditional multi-domain networks
  Lack of real-time, global network view
  No network resource allocation scheme
Performance
  Low concurrency, low link utilization, long transfer delay

## Slide 4
Source
Destination
100Gbps full duplex link
Site 1
Site 2
Site 3
Site 4
Site 5
Site 6
Site 7
SW1
SW2
SW3
SW5
SW6
SW7
SW4
Dataset X (3000 50GB files)
Case Study: Distribution Dataset X to All the Sites

## Slide 5
Scheduling Policy Computed by PhEDEx
Site 1
Site 2
3000 files
16.7Gbps
Site 1
Site 5
3000 files
16.7Gbps
Site 1
Site 3
3000 files
16.7Gbps
Site 1
Site 6
3000 files
16.7Gbps
Site 1
Site 4
3000 files
16.7Gbps
Site 1
Site 7
3000 files
16.7Gbps
Link Utilization:
Only Site 1 can be the source
Site 1 sends all 3000 files to each destination site
  Scheduling decision: (File K, site 1, site X) where K=1, 2, …, 3000 and X=2, 3, … 7
Leaves the bandwidth allocation to TCP
  Fair share of each site-to-site flow converges at 100/6=16.7Gbps

## Slide 6: ExaO: Software Defined Data Transfer Orchestrator
Leverage the emerging SDN technique to realize end-to-end orchestration of data flows involving multiple host groups at different domains
Key Features
On-demand, dynamic, minimal network state abstraction to provide global, real-time, inter-domain network view
Centralized, file-level transfer scheduling to achieve high transfer concurrency
Global, dynamic network resource allocation among flows to achieve high network utilization and low transfer delay

## Slide 7
ExaO: Software Defined Data Transfer Orchestrator
PhEDEx
Dataset level scheduling
Destination sites cannot become candidate sources until receiving the whole dataset
Low concurrency
Scheduler
Centralized file level scheduling
Destination sites become candidate sources after receiving files
High concurrency
No network resource allocation scheme
Low utilization
Scheduler and Transfer Execution Nodes (TEN)
Global, dynamic rate allocation among transfers (Scheduler)
End host rate limiting to enforce allocation (TEN)
ExaO
No real-time, global network view
Application-Layer Traffic Optimization (ALTO)
Collect real-time routing information at different domains (ALTO-SPCE)
Compute minimal, equivalent abstract routing state (ATLO-RSA)

## Slide 8
Kibana Monitoring
Kibana Monitoring
ExaO
Rest Interface
ExaO
Rest Interface
ExaO
RESTful Interface
DB
Kibana Monitoring
Monalisa
ExaO
Rest Interface
ExaO
Rest Interface
Scheduler
ExaO
Rest Interface
ExaO
Rest Interface
Transfer Execution Nodes
FDTDaemon
FDTDaemon
FDTDaemon
MLSensor
MLSensor
MLSensor
PhEDEx
ASO
Batch
ALTO
ExaO: Software Defined Data Transfer Orchestrator
Users submit dataset transfer requests
Update database
Query new requests
Collect complete network state
Query abstract routing state
Compute complete and abstract routing state
Dynamic Scheduling
Query updated scheduling
Enforce scheduling
Monitor Transfer Status
Update database
Install
flow rules

## Slide 9
PhEDEx
ASO
Batch
ExaO
RESTful Interface
MLSensor
FDTDaemon
MLSensor
FDTDaemon
MLSensor
FDTDaemon
Database
Scheduler
Transfer Execution Nodes
Kibana
Monitoring
MonALISA
ALTO Controller
ALTO Controller
ALTO Controller
Users submit, track and manage dataset transfer requests
Scheduler queries NEW requests via ExaO RESTful interface
Scheduler queries ALTO controllers for routing state
ALTO controller collects complete network state
ALTO controller computes on-demand, minimal, abstract routing state in response to query
Scheduler makes centralized, dynamic, file-level scheduling and global network resource allocation decisions
Transfer Execution Nodes (TEN) query updated scheduling and allocation decisions
TEN instruct efficient data transfer tools on end hosts (e.g., FDT) to enforce scheduling and allocation decisions
MonALISA sensors monitor data transfer status and send update back

## Slide 10
RESTful-API: allow users submit and manage transfer request through different interface
ALTO: collect on-demand, real-time, minimal abstract routing information from different domains
ExaO Scheduler: centralized, efficient file-level scheduling and network resource allocation
FDT: efficient data transfer tools on end hosts
Monalisa: Distributed monitoring infrastructure for real time monitoring of each flow, transfer
Components of ExaO

## Slide 11
Minimally invasive change on end host groups
Real-time, dynamic resource allocation under the existence of other network traffic
Not CMS or HEP specific, hence support any data intensive sciences.
Dataset distribution to N destination:
  Maximal link utilization in the testbed
  N times faster than dataset level scheduling
Practical Concerns

## Slide 12
Source
Destination
100Gbps full duplex link
Site 1
Site 2
Site 3
Site 4
Site 5
Site 6
Site 7
SW1
SW2
SW3
SW5
SW6
SW7
SW4
Dataset X (3000 50GB files)
Case Revisited: Distribution Dataset X to All the Sites

## Slide 13
Scheduling Policy Made by ExaO
Site 1
Site 2
Site 3
Site 4
Site 5
Site 6
Site 7
File 1-500
16.7Gbps
File 1-500
16.7Gbps
Site 1
Site 7
Site 2
Site 3
Site 4
Site 5
Site 6
File 2501-3000
16.7Gbps
File 2501-3000
16.7Gbps
Link Utilization:
(Maximum)
Site 1 is the only source at the beginning
Each site can become a source once receiving certain files
Site 1 sends 3000/6=500 unique files to each destination site
  Fair share of each (site 1, site X) flow is 100/6=16.7GB/s
  Remaining uplink bandwidth of site 1 is 0GB/s
After receiving a unique file from site 1, site X becomes a source to other destination sites
Site X sends the received file to other destination sites at (100-16.7)/5=16.7GB/s

## Slide 14
A user submits a request:
  {
  “DatasetName”: “A”,
  “Destination”: {“Site 2”, “Site 3”, “Site 4”, “Site 5”, “Site 6”, “Site 7”}
  }
ExaO receives this request and makes online file-level scheduling to maximize network utilization
Audience observe the scheduling decision made by ExaO and the high link utilization from testbed UI, and observe the status of file transfers through Monalisa
Demo: