## Slide 1: Problem
Super computing can benefit from super efficient and super flexible infrastructures
Traditional networks are not flexible, leading to inefficient network resources usage
Emergence of SDN promises super efficient and flexible networks but current SDN control programming systems are low level, limited (machine code age…)
Key feature | Issue
SDN programmer manually generates OpenFlow rules | OpenFlow is a low level, complex computation model: it does not even support logic negation, and hence needs priority to simulate logic negation, it supports only layer 2 to layer 4, but many decisions may depend on higher layers
SDN programmer uses incremental programming | Complex manual tracking of execution dependency Manual cleanup, re-execute
[TODO: Add more]… | 

## Slide 2: Toward Super SDN Programming: New SDN Programming Tools
Powerful state of the art, generic tools to substantially simplify SDN programming
Before (low level, limited programming model)
Low-level, complex, limited (L2-L4) OpenFlow rule programming
Programmer can define only at flow level
Specific access control allowing only hosts partition
Maple programming (high-level, all-layer programming)
High-level, completely south-bound agnostic, cross-layer (L2-L7) programming
Programmer sees (logically) each and every packet
Integrated access control supporting per-user or role based programming
FAST (automation function store)
Automatic execution dependency tracking
Automatic cleanup, re-execution (intent ++)
Host generic network functions
Before (raw data store)
Complex, manual tracking of execution dependency
Manual cleanup, re-execute
Designed directly on raw data store
Data Store
Before (manual programming)
Complex, manual maven programming
Web IDE
Web-based automatic generation of projects
Programmer focuses only on key aspect
Before
Ad hoc flow rule installation
FAST Schedule
Consistent, optimized flow-mod scheduling

## Slide 3: The Super Simple SDN Programming Model
Consider each pkt as a request
- Network as a single virtual server
- Network functions (logically) invoked on each new pkt, returning how net handles that request
- Network functions expressed in general purpose language
- Realization of return is opaque, by system
- Network decision can depend on L2 to L7
- Network decision is lambda decision, not incremental decision

## Slide 4: TODO: - Change to Final Program - Highlight key features, e.g., per-packet, cross layer (L7), meta control, …
void f(Packet p) {
if ( !permit(p) ) p.route = null;
else {
EndpointProp sedp = hostTable(p.ip.ipSrc());
EndpointProp dedp = hostTable(p.ip.ipDst());
int rate = p.te.vRate(); // custom protocol
QoSRoute qr = routingAlg(sedp, dedp, rate);
p.route = qr.route; p.vrate = qr.rate;
}
}
QoSRoute routingAlg(EndpointProp s, EndpointProp d, int r) {
if ( allowedRate(s, d) < r ) // authorization
r = allowedRate(s, d);
return QoSRouting(s, d, r);
}
Per-packet programming model
Standard+Custom protocols
Meta header to control cross layers
Notes: relatively low rate, unreliable, nodes are highly mobile

## Slide 5: Demo: Realizing Super Simple SDN Programming using OpenFlow, Bro
TODO: Draw network, label what each component does

## Slide 6: Backup Slides

## Slide 7: High-level SDN Programming Abstraction: Function Store (Details; skip)
function instance
public void QoSRouting(Ipv4Address src, Ipv4Address dst, int requiredBw) {
srcNode, dstNode = mapToNode(src, dst);
topology = readTopology();
pq.add(srcNode);
while (!pq.isEmpty()) {
n = pq.pop();
if (bw_src(n) < requiredBw)
return failure
if (n == dstNode)
return writeRoute(src, dst, path);
for (e(n->m): n.neighbors) {
if (min(e.bw, bw_src(n)) > bw_src(m)) {
updateBw(m, min(e.bw, bw_src(n)));
...
}
}
}
return failure }
    Allow generic functions
    Automatically track data dependency
    Automatic clean up, reschedule, and re-execute after dependent data changes (achieve intent)
function instance
function instance

## Slide 8
New Tools in Action: Programmable Science DMZ
Bro
function cloud
Bro
Bro
transport network
RESTCONF /YANG Data Store
Data-driven function/transport control
TO FINISH

## Slide 9: Problem
Super computing can benefit from super efficient and super flexible infrastructures
Traditional networks are not flexible and often cannot use network resources efficiently
Emergence of SDN promises super efficient and flexible networks but current SDN control programming systems are low level, limited in key capabilities
Network State
Datapath Model
Service/ Policy
Datapath Model
Program Logic